Intro to Embedded Reverse Engineering for PC reversers
Igor Skochinsky
Hex-Rays
Recon 2010
Montreal

---
Outline
- Embedded systems
- Getting inside
- Filesystems
- Operating systems
- Processors
- Disassembling code

---
Embedded systems
- Highly integrated
- Designed as a single unit
- Not much configurability
- Emphasis on size and power consumption
- Reversing challenges
  - Many variations
  - New architectures/instructions set
  - Difficult to find information
  - No conveniently named APIs

---
Getting inside
- First step: getting the code
  - Firmware updates
  - Serial port
  - Communication with PC
  - JTAG
  - Flash chip dumping
  - Exotic ways

---
Getting inside: firmware updates
- Most manufacturers provide updates for devices
- Simplest way to get code if not encrypted/obfuscated
- Usually comes in one of two flavors:
  - An updater program to run on PC (includes the actual update file, separately or embedded)
  - Just an update file to be copied to the device manually

---
Getting inside: firmware updates
- Update files can contain:
  - Filesystem images
  - Kernel images
  - Bootloader images
  - Updater programs or scripts
  - Some (or all) of them can be compressed
- Look for big chunks of 00s or FFs delimiting the parts
- Check for common compression stream patterns
  - zlib: 78 01, 78 9C, 78 DA
  - gzip: 1F 8B
  - LZMA: 5D 00 00 80

---
Getting inside: firmware updates example 1
- Sony Librie (the first E-Ink ebook reader)
- Includes UPLIBRIE.exe, EBRCTR.dll and data.bin
- data.bin contains several images encrypted with a fixed XOR key
- Decryption is done on PC side, so images are easily recovered

---
Getting inside: firmware updates example 2
- Intel SSD drive
- Update is a bootable FreeDOS CD ISO
- Actual updater is a 32-bit DOS program (LE), compiled with Watcom (iSSDFUT.exe)
- Firmware images are compiled in as byte arrays
- Need to be identified by following program logic
- ATA command DOWNLOAD MICROCODE is used
- Each image is 256000 bytes

---
Getting inside: firmware updates example 3
- Amazon Kindle
- Firmware update is an obfuscated .bin file
- The file needs to be copied to the Kindle's USB drive
- Update process triggered by user command
- De-obfuscation and unpacking is done on the device
- Thus the code has to be extracted with other means
extract_bundle()
{
    dd if=$1 bs=${BLOCK_SIZE} skip=1 | dm | tar -C $2 -xzvf -
}

---
Getting inside: serial port
- Also known as UART (universal asynchronous receiver/transmitter), or just "COM port"
- Used during development and diagnostics
- Allows access to the bootloader and/or main OS
- Getting the code usually involves these steps:
  - Find UART parameters
  - Get/make the cable
  - Identify on board
  - Download the code

---
Getting inside: UART parameters
- Necessary to get the correct data from the device, since protocol is sensitive to timing
- Best source is Linux/bootloader sources if manufacturer provides them
- Grep for "uart”, "serial”, "console”.
- Otherwise, the most common settings are:
  - For Linux devices, 115200 8n1
  - For Windows CE devices, 38400, 8n1

---
Getting inside: serial cable
- Devices operate on TTL levels (0/3.3V or 0/5.5V)
- PC COM port operates on RS-232 levels (up to +/-15V)
- Need a level converter
  - Self made: using a MAX232/3232 chip or analog
  - USB-TTL converter: using FT232/2232 chip
  - Phone cable: many mobile phones actually used serial port to communicate with PC
  Many such converters are available pretty cheap on Ebay

---
Getting inside: UART identification on board
- Three or four pins are used: TX, RX, GND (and Vcc)
- Check for groups of four pins on board
- Otherwise, can be found by trial and error
  - GND: use metallic shields or connector housing
  - Start up terminal program, attach RX to potential TX pin, reset device
  - Repeat until you get something on the screen
  - RX is usually nearby and often
    you can see the echo from
    typing

---
Getting inside: getting code via UART 1/3
- If you get to login prompt, try some obvious logins/passwords
- E.g. root/root, root/admin, root/<device name>
- Once logged in, you can usually copy the files somehow
  - USB partition: if there's a partition that's visible on the PC, you can copy files there
  - Connect/disconnect USB or insert a memory card to see if the filesystem changes
  - Check /etc/fstab, init scripts for mention of external filesystems

---
Getting inside: getting code via UART 2/3
- Another way is to dump the complete flash
- Linux usually uses MTD (Memory Technology Devices) translation layer to handle flash partitioning
- To see the flash map:
  cat /proc/mtd
- To copy a partition:
  dd if=/dev/mtdN of=/tmp/dumpN
dev: size erasesize name
mtd0: 00200000 00010000 "sdm device NOR 0"
<...>
mtd11: 00160000 00020000 "Linux0"
mtd12: 007e0000 00020000 "Rootfs2"
<...>

---
Getting inside: getting code via UART 3/3
- If you can't login into Linux, you might be able to get into the bootloader
- There are many bootloaders used in embedded systems; Das U-Boot seems to be most common
- To stop in the bootloader you usually need to press a key shortly after reset
- Actual commands to use depend on the device (try 'help')
- For Kindle, I had to use the hex dump command, as there was no way to copy data over USB or to a memory card
check_recovery: shift-<r>ecover, shift-<u>pdate, shift-</> reset...
normal boot...
U-Boot 1.1.2 (Oct 29 2007 – 16:35:25)
*** Welcome to Kindle ***

---
Getting inside: misusing the PC communication
- Many manufacturers provide programs to communicate with the device from PC
- It's worth reversing the program to see what it does
- There might be hidden commands not available via the UI
- There might be legitimate commands that can be used in novel ways
- USB traffic spying might be useful

---
Getting inside: misusing the PC communication example 1
- Sony Reader PRS-500
- Was bundled with "Sony CONNECT Library”
- The program copied ebooks to the device
- Ebooks went into the directory /Data/
- Protocol had "write”, "read”, "list” and "delete” commands
- Wrote a custom script that talked to interface DLL and could specify any path
- /proc/mtd and /dev/mtdN were accessible this way
- The complete fimware was downloaded

---
Getting inside: misusing the PC communication example 2
- Casio EX-Word electronic dictionary
- Casio offered free downloads of games to install on it
- Reversed the program used to install them
- Games were decrypted just before sending over USB
- Dumped decrypted games, spent some time reversing
- Eventually found references to savefile
- Replaced savebuffer address with system memory's
- Uploaded modified game; instead of savedata system memory was saved to file
- By "unloading” the game, could get the savefile back
- Dumped system memory (the OS) in chunks

---
Getting inside: JTAG
- Joint Test Action Group
- Originally developed for testing circuit boards
- Many microcontrollers add commands for debugging
- Allows complete control over the processor
- Can be used to download and upload flash
- Needs an adapter
- Pins are not always obvious; programs exist to brute-force the layout
- Another option is to trace pins from the processor (might need desoldering)

---
Getting inside: Flash chip dumping
- The actual flash content is (so far?) rarely encrypted
- So dumping the chip itself (if it is separate) is an option
- Sometimes can be done in-place, but usually requires desoldering the chip
- Best done by an experienced person

---
Getting inside: exotic ways
- CHDK project (custom fimware for Canon cameras)
- Used the camera LED to dump the firmware
- Firmware bits were transmitted as LED light pulses with some redundancy and error checking
- Pulses were recorded as sound via a phototransistor
- Resulting waveform was decoded to binary data

---
Embedded filesystems
- Embedded systems often use special filesystems
- Space is limited, so compression is used
- Read-only filesystems for permanent files (rootfs)
- Flash wear should be taken into account
- Most common filesystems nowadays:
  - cramfs
  - SquashFS
  - JFFS2
  - YAFFS
  - others (VFAT, ext2, minix, UBIFS)

---
Embedded filesystems: cramfs
- Stands for "Compressed ROM file-system"
- Read-only filesystem
- Files are compressed with zlib (aka deflate)
- Has some limitations, so getting less popular
- Signature magic: 0x28CD3D45
- To unpack: cramfsck -x <dir> image.cramfs

---
Embedded filesystems: SquashFS
- Another compressed read-only filesystem
- Can use zlib or LZMA
- Present in mainline Linux
- Was used in Kindle
- Signature magic: 0x73717368 ("sqsh")
- To unpack: unsquashfs -d <dir> image.sqs

---
Embedded filesystems: JFFS2
- Journalling Flash File System 2
- Used when writable FS is needed (e.g. user files)
- Designed to reduce flash wear
- Has several compression algorithms
- Signature magic: nodes start with 0x1985
- Official way to unpack involves Linux and MTD devices
- Wrote a Python script to do it in one go on any platform

---
Embedded filesystems: YAFFS
- Yet Another Flash File System
- Recently popularized by use in Google Android
- Also designed for flash chips
- No dedicated magic
- Tends to begin with 03 00 00 00 01 00 00 00 FF F
- To unpack: unyaffs image.yaffs

---
Embedded filesystems: others
- ext2/ext3: sometimes used even though not optimized for flash
- VFAT: used as backing FS for mass-storage devices
- UBIFS: "successor" to JFFS2, used in N900
- LogFS: another successor
- minix
- romfs – used for initial ramdisk inside the kernel
- Propietary/non-Linux
  - Microsoft: TFAT, TExFAT
  - Samsung: TFS4 (Transactional File System 4), RFS (Robust FAT File System)
  - Wind River: TrueFFS

---
Embedded Operating Systems
- Embedded devices are constrained by processing power and memory
- Simplest devices do not use any OS at all
- RTOS (Real-time OS)
  - Emphasis on fast reaction to events and predictability
  - Handles narrow set of tasks
  - Provides basic functionality for running tasks (or threads), sync primitives, messaging and other APIs
  - Can be very small, from a few KB
  - Tasks usually fixed at compile time and linked into final image
- Linux is used for "bigger", usually CE devices

---
Embedded operating systems: Linux
- Gets more and more widespread
- Generally needs a processor with MMU (Memory Mapping Unit); MMU-less variant exists (uCLinux)
- Due to GPL sources have to be provided by the maker
- Thus often easiest to reverse
- Needs a bootloader; Das U-Boot used often
- WebOS (Palm) and Android (Google) are also based on Linux
- Identification: "Linux" is usually present somewhere in the image or in the boot output; also check maker site for sources

---
Embedded operating systems: Nucleus RTOS
- A small RTOS from Mentor Graphics
- Distributed in source form (NOT open source)
- Mostly written in C with few processor-specific parts
- Used in many mobile phones (Siemens, Samsung etc)
- Example ID string:
  Copyright (c) 1993-2002 ATI - Nucleus PLUS - Integrator ADS v. 1.13.4

---
Embedded operating systems: VxWorks
- RTOS, made by Wind River Systems (bought by Intel)
- Used in:
  - Network appliances (home routers/modems)
  - Set-top boxes, DVD players
  - Even in spacecraft (Mars rovers Spirit and Opportunity)
- Example ID string:
  Copyright 1999-2001 Wind River Systems, Inc.
- http://chargen.matasano.com/chargen/2008/4/29/retsaot-is-toaster-reversed-quick-n-dirty-firmware-reversing.html

---
Embedded operating systems: Windows CE
- Written from scratch RTOS with Win32 APIs
- Pretty popular due to low licensing charges and familiar API
- First versions ran on ARM, MIPS, PowerPC, SuperH, x86
- Now only ARM and x86 officially supported
- Pocket PC, Windows Mobile run on Windows CE kernel
- Not just phones, also common on GPS devices and other portable devices (e.g. Panasonic Words Gear)
- ID string: "CECE" at offset 0x40

---
Embedded operating systems: others
- QNX, ThreadX, µC/OS-II
- Symbian
- eCos
- TRON (ITRON, BTRON etc): a common RTOS specification/interface used mostly by Japanese makers
- Sometimes chip manufacturers offer a standard OS
  - SuperH: HI7700/4 for from Renesas

---
Embedded processors
- Microcontrollers vs. microprocessors
- RISC vs. CISC
- Common processors

---
Embedded processors: microcontrollers vs. microprocessors
- Microprocessor:
  - Includes processor core (decoder, ALU, registers etc)
  - Interfaces with extra controllers for RAM, ROM and other peripherals
  - General-purpose
- Microcontroller:
  - Besides processor core, integrates RAM, program ROM (often Flash ROM), and peripherals
  - Thus commonly called "System-on-Chip" (SoC)
  - Specialized
  - In the same family many variations exist with different sets of peripherals tailored for different tasks

---
Embedded processors: microcontrollers vs. microprocessors
System-on-Chip
Modern PC
Image: wiki commons/Cburnett, CC-BY-SA-3.0
Image: wiki commons/David Futcher, CC-BY-SA-3.0

---
Embedded processors: RISC vs. CISC
- RISC: Reduced instruction set computing
  - Basic strategy: simple instructions that execute quickly
  - Most instructions usually need one cycle
  - Short, fixed-length encodings (commonly 2/4 bytes)
  - Load/store architecture
  - Orthogonal instruction set and registers
- CISC: Complex instruction set computing
  - Complex instructions that do complex things
  - Often use complex, multi-byte instruction encodings
  - Specialized registers for some operations
- In recent years the boundary between RISC and CISC is getting blurry

---
Embedded processors: ARM
- Flat 4GB memory space
- Actual layout depends on the chip
- Reset entry: 0 for "classic" ARMs
- Usually has B xxx (0xEAxxxxxx) or LDR PC (0xE59FFxxx) there
- For Cortex-M: value at 0 is initial SP, at 4 – initial PC
- Common patterns:
  - ARM mode (little-endian): xx xx xx Ex (always-executing instruction)
  - Thumb mode (little-endian): 47 70 (BX LR), xx B5/xx B4 (PUSH)

---
Embedded processors: MIPS
- Memory usually divided in several segments with different virtual addresses mapping to the same physical address
- Reset entry: virtual 0xBFC00000, physical 0x1FC00000
- Usually has a branch there: 0x1000xxxx
- Common patterns:
  - 03 E0 00 08 (jr $ra – return)
  - 3C xx xx xx (lui)
  - 24 xx xx xx (addiu)
  - 1x xx xx xx (branches)
  - 0C xx xx xx (jal)

---
Embedded processors: PowerPC
- Flat 4GB memory space (for 32-bit version)
- Reset entry: 0xFFFFFFC for "Book E" (embedded) variant
- 0x100 or 0xFFF00100 for "classic" PPC
- Common patterns
  - 4E 80 00 20 (blr – return)
  - 48 xx xx xx (branches)
  - 7C 08 xx A6 (mtlr %rx – save link register)

---
Embedded processors: 8051
- Probably the most ubiquitous microcontroller architecture
- Developed in 1980, new models still appear today
- Harvard architecture (instructions separately from data)
- Bit-addressing instructions
- Reset vector: 0000H
- Common patterns
  - 02 xx xx (ljmp – absolute jump)
  - 22 (ret)
  - C2 xx, D2 xx (clr – clear bit, setb – set bit)

---
Embedded processors: Others
- 32-bit
  - M68K: CPU32, ColdFire (CISC)
  - SuperH (RISC with 16-bit instructions)
  - M32R
  - NEC V850, 78K0
- 8-bit
  - Microchip PIC
  - Atmel AVR
  - 68HC08, 68HC11
- Identification
  - Search for the chip markings
  - Check the manufacturer logo:
  http://www.elnec.com/support/ic-logos/?method=logo

---
Disassembling code
- After getting the code and identifying processor, next step is the actual disassembly
- Common image formats
  - ELF
  - OS-specific
  - Kernel images
- Raw binary
- Recovering symbol information

---
Disassembling code: ELF
- Executable and Linkable Format
- Was developed for use on UNIX systems
- Nowadays used in other embedded systems and even OS-less environments
- Many tools available
  - binutils: objdump, objcopy
  - IDA Pro
  - pyelf
- Format specifies loading addresses
- For a common processor usually no extra work required
- Less common processors might need some manual work (relocations, imports etc.)

---
Disassembling code: OS-specific formats
- Some OSes use custom formats
- Windows CE: PE files
- iOS (formerly iPhone OS): Mach-O
- Symbian: EPOC
- Unix 'file' command can be useful in identifying formats
- Also objdump from binutils (compile with --enable-targets=all)

---
Disassembling code: Kernel images
- Often kernel is a structured image itself, e.g. an ELF or Mach-O file
- However, often this is not the case
- Usually one of two options is used
- 1) Image is prepared to be run from a specific address, where it is loaded by bootloader
- 2) A small bootstrap is prepended to the kernel ('piggy' in Linux terms), which unpacks or just copies the rest of the image to the final location, then jumps to it
- For ARM Linux kernel, you can extract the final image by looking for gzip signature (1F 8B) and extracting the data from there

---
Disassembling code: raw binary
- Sometimes there are no structured files, just binary code
- First you need to determine the load base
- A good first try would be just to load it at 0 and see if things match up
- Otherwise try to use hints from the code
  - Self-relocating code
  - Initialization code
  - Jump tables
  - String tables

---
Disassembling code: raw binary, self-relocating code
- Self-relocating code copies itself to proper address if running from a different one
- This way you can also determine exact boundaries of the code fragment
00000040 MOV R0, PC ; R0 = current address + 8
00000044 LDR R1, =0x48 ; subtract 0x48 to get the load base
00000048 SUB R0, R0, R1 ; R0=load base
0000004C LDR R1, =0 ; 0 is the preferred load base
00000050 CMP R0, R1 ; are we at the preferred base?
00000054 BEQ loc_78 ; if yes, continue
00000058 LDR R1, =0 ; R1 = target
0000005C LDR R2, =0xB000 ; R2 = count
00000060 copyloop
00000060 LDR R3, [R0],#4 ; load word
00000064 SUBS R2, R2, #4 ; decrease counter
00000068 STR R3, [R1],#4 ; store word
0000006C BNE copyloop ; repeat until done
00000070 LDR R1, =0 ; load the new address
00000074 BX R1 ; branch to it

---
Disassembling code: raw binary, initialization code
- Initial code usually runs from flash
- But the main program needs writable data, both initialized (.data) and uninitialized (.bss)
- The usual algorithm of the startup code:
  - Copy code for faster execution to RAM (optional)
  - Copy initialized data from read-only memory to RAM corresponding to .data segment
  - Zero out the uninitialized data area (.bss)
- Identifying these steps can help to determine the actual load address of the code

---
Disassembling code: raw binary, jump tables
- Compilers often implement switch statements with jump tables
- Offsets in the jump table should point to valid code near the indirect jump instruction
1001458C CMP R2, #3 ; switch 4 cases
10014590 LDRLS PC, [PC,R2,LSL#2] ; switch jump
10014594 B loc_100145E0 ; default
10014594 ; --------------------------------------------------------------
10014598 DCD loc_100145A8 ; jump table for switch statement
10014598 DCD loc_100145AC
10014598 DCD loc_100145AC
10014598 DCD loc_100145D8
100145A8 ; --------------------------------------------------------------
100145A8 loc_100145A8
100145A8 B loc_100145E0 ; jumptable 10014590 case 0

---
Disassembling code: raw binary, string tables
- Sometimes the program uses a table of strings
- It is usually represented by an array of offsets to strings
- By subtracting offsets you can get lengths of strings
- Those can then be matched against strings in the binary
- This can even be automated

---
Disassembling code: recovering symbol information 1
- When disassembling raw binaries, you don't have nice API names as with user-mode apps
- However, kernels often include symbol tables, to simplify debugging and provide better stack traces for crash dumps
- For a running Linux kernel, symbol table can be extracted by reading /proc/ksyms or /proc/kallsyms
- In 2.4 kernels a simple <address, name> table was used
- In new kernels a compressed format is used, see kallsyms.c
- Wrote a Python script to extract them

---
Disassembling code: recovering symbol information 2
- Other binaries might use simple symbol tables too
- E.g. VxWorks:
  struct _SYMBOL {char *name; char *value; SYM_TYPE type; UINT16 group;};
- Search for "panic", "trace", "exception" or "assert".
- Often such functions get passed a function or source file name
- Once you identify some function names, search Internet for them, you might find where they came from
- If reversing a known OS, check official sites for demo/eval versions; even if for different processor, you can often match the code flow and identify other matches
panic("start_stop_timer", "start_stop_timer: timer %d not supported\n", id);
_assert("Assertion failed: pGraph!=((void *)0), CA_Connection.c, line 89\n");

---
Disassembling code
Demo

---
Conclusion
- Embedded reversing can be quite different
- However, some skills can be reused
- A lot of information is available if you know what to look for
- Can be a very rewarding process
- A goldmine if you're into vulnerability research
- Some links
  - igorsk.blogspot.com
  - www.lostscrews.com
  - mbed.org

---
Thank you!
Questions?